## Slide 1: F`Software Framework A Small Scale Component Framework for Space
Jet Propulsion Laboratory,
California Institute of Technology
10/3/2020
© 2009-2020 California Institute of Technology. Government sponsorship acknowledged.
ALL RIGHTS RESERVED. acknowledged.
This software has been approved for open source release under NTR #49404.

## Slide 2: What is F´?
Embedded Systems Framework
Flight Software for Small-Scale Projects
  Cubesats, Deployables, Instruments
Provides:
  Framework Autocoder
  Standard Components and Abstractions
  Modeling, Testing, and Basic Ground Support
Credit: NASA – 2015

## Slide 3: Why F´?
Standard Components and Abstractions
Flight Heritage
Designed For Modularity and Reuse
Compact Code, Efficient Implementation
Scalability Features
Unit Testing Framework
Credit: JPL/NASA – Artist’s Concept

## Slide 4: Background
F` was developed as part of a technology development task at JPL
  Explore new flight hardware
  Explore new software approaches
  Targeted at smaller projects like instruments, Cubesats, and Smallsats
  Sparser processor resources
    Lower amounts of memory, storage, and processor computing power
    Microcontrollers, small embedded processors, radiation-hardened avionics
  Clusters of interconnected processors
Goals were to show:
Goal | Explanation
Reusability | Frameworks and adaptations readily reusable
Modularity | Decoupled and easy to reassemble
Testability | Components easily isolated for testing
Adaptability | Should be adaptable to new contexts and bridge to inherited
Portability | Should be portable to new architectures and platforms
Usability | Should be easily understood and used by customers
Configurability | Facilities in the architecture should be scalable and configurable
Performance | Architecture should perform well in resource constrained contexts. Should be very compact.

## Slide 5: F`: A Component Architecture
Definition: The F` Component Architecture is a design pattern based on an architectural concept combined with a software architectural framework.
Not just the concepts, but framework classes and tools are provided for the developer/adapter.
Implies patterns of usages as well as constraints on usage.
Centered around the concept of “components” and “ports”
Uses code generation to produce code to implement common framework patterns and facilities
  Developer specifies in XML (soon to develop DSL)
Developer writes implementation classes to implement interfaces.
Component
Component
Component

## Slide 6: Characteristics of Components
Encapsulates behavior
Components are not aware of other components
Localized to one compute context
  e.g. physical processor, user process, etc
Interfaces are via strongly typed ports
  Ports are formally specified interfaces
  There are no direct calls to other components
Context where software threads run
Where flight/ground commands, telemetry and parameters are defined
Component
1
2
3
Port 1
Port 2

## Slide 7: Characteristics of Ports
Encapsulates typed interfaces in the architecture.
  Implemented as C++ class with one interface method
Point of interconnection in the architecture
Ports are directional; there are input and output ports
  Direction is direction of invocation, not necessarily data flow. Ports can retrieve data
Ports can connect to 3 things:
  Another typed port
    Call is made to interface method on attached port
  A component
    Incoming port calls call component registered callback
  A serialized port
    Port serializes call and passes as data buffer (more to come)
All arguments in the interface are serializable, or convertible to a data buffer. There are built-in types supported by the framework; developer can write custom types. (see later slides)
Ports can have return values in limited cases
  Only able to return data when component has synchronous interface (see definition later)
  Serializable connections are defined as only output data flow
Pointers/references are allowed for performance reasons
  User beware!
Multiple output ports can be connected to a single input port, but only one port connection for each output port.
Component
1
2
3
serialize()

## Slide 8: A Component Topology
Component 1
1
2
3
Port 1
Port 2
Component 2
1
2
3
Port 1
Port 2
Component 3
1
2
3
Port 1
Port 2
Components are instantiated at run time
They are then connected via ports into a Topology, or a specific set of interconnected components
There are no code dependencies between components, just dependencies on port interface types
Alternate implementations can easily be swapped
  Simulation versions, alternate drivers, etc.

## Slide 9: Component Type Hierarchy
Hierarchy consists of:
  core framework classes
  generated classes that implement architecture features
  Developer written classes that implement interface handlers and project-specific logic

## Slide 10: Component Types
User specifies type of component in XML. Types are:
Passive Component
  No thread
  Input port interface calls are made directly to implementation class handler methods on the thread of the caller of the input port.
Queued Component
  No thread, adds a message queue
  Asynchronous port calls are placed on component message queue.
  Implementation class calls method in base class on the thread of another caller to dispatch any messages pending in the queue.
Active Component
  Component has thread of execution as well as queue
  Thread dispatches port calls from queue as it executes based on thread scheduler
Calls to output port are on thread of implementation functions
  Thread making call is dependent on port type (see next slide)

## Slide 11: Port/Component Characteristics
The way incoming port calls are handled is specified by the component XML.
Input ports can have three attributes:
  Synchronous – port calls directly invoke derived functions without passing through queue
  Guarded – port calls directly invoke derived functions, but only after locking a mutex shared by all guarded ports in component
  Asynchronous – port calls are placed in a queue and dispatched on thread emptying the queue.
A passive component can have synchronous and guarded ports, but no asynchronous ports since there is no queue. Code executes on the thread of the calling component.
A queued component can have all three port types, but it needs at least one synchronous or guarded port to unload the queue and at least one asynchronous port for the queue to make sense. Code executes on the thread of the caller.
An active component can have all three varieties, but needs at least one asynchronous port for the queue and thread to make sense. Code executes on the thread of the caller or component depending on port type.
Developer needs to be aware of how all the different call kinds interact (e.g. reentrancy)
Output ports are invoked on the thread of handlers by calling methods in the generated base class.
Code Generated Active Base Class
port1()
virtual func1()=0
Developer Written Implementation Class
handler1() {…
func4()
}
Task
Asynchronous
port2()
handler2()
{…}
Synchronous
port3()
handler3()
{…}
Guarded
func4()

## Slide 12: Serialization
Serialization is a key concept in the framework
Definition: Taking a specific set of typed values or function arguments and converting them in an architecture-independent way into a data buffer
Asynchronous port calls and commands and their arguments are serialized and placed on message queues in components
Commands, telemetry, and parameters are specified as serializables for transport to and from ground software
User can use built-in types or define complex types in XML and code generator will generate serializable classes that are usable internally as well as interfaces to and from ground software
User can also implement arbitrary serializable types with a set of required methods and the framework automatically handles them

## Slide 13: Serialization Ports
A special optional port that handles serialized buffers
Takes as input a serialized buffer when it is an input port, and outputs a serialized buffer when it is an output port.
Can be connected to *any* typed port (almost).
  For input port, calling port detects connection and serializes arguments
  For output port, serialized port calls interface on typed port that deserializes arguments
  Not supported for ports with return types
Useful for generic storage and communication components that don’t need to know type
  Allows design and implementation of C&DH (command and data handling) components that can be reused.
Comp1
Comp2
Typed port
Serialized port
Comp3
Serialized port
Typed port

## Slide 14: Commands, Telemetry, Events and Parameters
The code generator provides a method of implementing commands, telemetry, events (AKA EVRs), and parameters for interface with a ground system.
Component XML specifies arguments and types.
Data for service is passed in serialized form.
The generated code decodes serialized commands and invokes implementation handlers with the correct arguments. Telemetry and events are emitted by calling typed functions from implementation code.
Port types for flight/ground interface are defined in normal XML, so they can be used by the code generator for implementing component-level handlers or generically by other components used to implement flight/ground functions.

## Slide 15: Commands
Component command XML specifies:
  Opcode, mnemonic, and arguments
    Arguments can be any built-in type or developer defined enumeration
  Synchronization attribute
    Sync, async, or guarded
    Same meaning as ports
      Async can specify message priority
Implementation class implements handler for each command
  Base class deserializes arguments from argument data buffer
Implementation class reports a command status when done
  Can be immediately in handler or deferred until command is complete later
  Component must report a status to clear command dispatcher tracking and advance sequences
Autocoder automatically adds ports for registering commands, receiving commands and reporting an execution status.

## Slide 16: Events
Component event XML specifies:
  ID, name, severity and arguments
    Arguments can be any built-in type or XML complex type
    Can define enumerations
  Format specifier string
    Used by ground software and optional on-board console to display message with argument values
    Follows C format specifier syntax
Code generated base class provides method to call for each event with typed arguments
  Provides stronger type checking at compile time than MER/MSL EVR macros
  Called by implementation class
  Automatically time-tags event at moment of method invocation
Code generator automatically adds ports for retrieving time tag and sending event
  Two independent ports for sending events
    A binary version with serialized arguments for transport to ground software
    A text port that sends a string version of the event (using the format specifier) that can be sent to a console
      Can be globally disabled via architecture configuration macros to save execution time and code space

## Slide 17: Telemetry
Component telemetry XML specifies channels that have:
  ID, name, and data type
    Data type can be any built-in type or external XML complex type
    Can define enumerations
  Format specifier string
    Used by ground software and optional on-board console to display message with argument values
Code generated base class provides function to call for each channel with typed argument
  Called by implementation class
Code generator automatically adds ports for retrieving time tag and sending channelized data

## Slide 18: Parameters
Parameters are traditional means of storing non-volatile state
  Framework provides code generation to set and save, but developer must write a component to load and save parameters from a particular non-volatile storage
    File-based implementation provided with distribution
Component XML specifies parameters that have:
  ID, name, and data type
    Data type can be any built-in type
    Can define enumerations
  Optional default value
    In the event the parameter cannot be retrieved, assigns default value to parameter
Code generator generates commands for setting and saving parameter values
Code generator generates optional overridable virtual method for providing notification to implementation class when values are updated.
Code generator automatically adds ports for retrieving and saving parameters
  When parameters are saved by commands at the component level, the “save” port sends the parameter value to the storage component. The storage component is responsible for when and how to save parameter value
During initialization, a public method in the base class is provided to load the parameters and store copies in private component data
Code generated base class provides function to call for each parameter to retrieve stored copy
  Implementation class can call whenever parameter value is needed
  Implementation class cannot modify the parameter value, only commands can

## Slide 19: Core Components
A set of core components has been matured over the lifetime of F’
  Some subjected to JPL class B flight processes
    Reviews, inspections, full coverage unit tests and static code analysis
  Some contributed back to F’ core repository by projects
Provides out-of-the box implementations so that projects don’t have to start from the beginning
Common command and data handling components
Flight/ground interface components
Drivers
Helper components

## Slide 20: Command Dispatcher (Svc/CmdDispatcher)
Command dispatcher is an active component
Components register their command opcodes
Command dispatcher receives buffer from ground or sequencer containing command and arguments
Command opcode is extracted, and opcode lookup is made
Component is invoked to execute commands it registered
Component responds with completion status (pass, fail) when command complete
CmdDispatcher
Mod1
ModN
OC
command
register
status
buffer
status

## Slide 21: Command Sequencer (Svc/CmdSequencer)
Command sequencer loads file from file system
Sends command and waits for response for each command in the file
A failed response terminates the sequence, successful response moves to the next command
Active component
Command
Dispatcher
1. command
CmdSequencer
File
2. status

## Slide 22: Channelized Telemetry (Svc/TlmChan)
Telemetry database has double-buffered array of telemetry buffers
Component writes updated value with time tag to telemetry database component
Telemetry database writes value to active buffer
Run port is called periodically by rate group. Swaps active buffer
Run call copies updated values to downlink
Active component
TlmChan
Component
value
Time
Component
time
1. write()
run
downlink
active

## Slide 23: Event Log (Svc/ActiveLogger)
Component sends time-tagged event to Event Log component
Event log component places event on message queue. Thread of Event Log component then sends downlink packet with event
FATAL event immediately invokes FATAL handler port on thread of calling component for special handling if desired
Active component
Component
3. event
ActiveLogger
Time
Component
2. time
Msg Q
4. downlink
1. event()
Fatal

## Slide 24: Parameter Database (Svc/PrmDb)
Parameter Database loads file containing parameters from file system during initialization
Initialization subsequently calls loadParameters() on all components with parameters.
Commands to components can update and set parameter values via port call to parameter manager
Manager can save updated values to file system via command
Component
get parameter
PrmDb
File
loadParameters()
set parameter
Parameter set/save commands

## Slide 25: Rate Group (Svc/ActiveRateGroup)
Rate group is a array of run() ports
Gets a call to asynchronous run port driven by project specific timing component
Calls ports in order
Since is a list of run ports, doesn’t know (or care) which destinations are in active components or not
Rate Group is an active component
Active
Rate
Group
run()
run()
active
run()
….
run()
run()

## Slide 26: Polymorphic Database (Svc/PolyDb)
Used to pass values around internally between components
Uses Fw/PolyType class to allow a range of types to be stored
  Enforces value type written is value type read
Stored as an array accessed by integer index
  Project assigns meaning to values stored with index
PolyDb
Component 1
get
Component 2
set

## Slide 27: Buffer Management (Svc/BufferManager)
Manages a pool of buffers for components
Variable sized buffers
FIFO based storage
Component gets() a buffer, uses it, and then sends() it when complete
Buffer lifetimes managed as a system issue
BufferManager
get()
send()

## Slide 28: File Downlinking (FileDownlink)
Sends the contents of a file to the ground system when commanded
Gets buffers from BufferManager
FileDownlink
File
BufferManager
Downlink
get()
send()

## Slide 29: Multi-node
Hub pattern
  Hub is a component with multiple serialization input and output ports
  Typed ports on calling components are connected to serialized ports (see earlier slides)
  Each hub instance is responsible for connecting to a remote node
  Input port calls are repeated to corresponding output ports on remote hub
  Single point of connection to remote node, so central point of configuration for transport.
Node 1
Producer
Component1
Transport (Socket, ARINC Channel, UART, IPC)
Node 2
Consumer
Component1
Hub
Hub
Consumer
Component2
Producer
Component2

## Slide 30: Typical F´ Application Architecture
Manager
Component
Manager
Component
Application
Component
Driver
Components
Driver
Components
Notes: Typically applications are layerd.

## Slide 31: Code Scaling
Framework code is very compact
Generated code is also compact
  Demo application for TI microcontroller was about 15K
Native type sizes can be configured
  e.g. some microcontrollers have 16-bit/8-bit only support
Features can be added or removed depending on resources
  Object naming
  Port execution tracing
  Serialization of ports
    Single node systems don’t really need
    This is not data serialization but the use of serialized ports
  Object naming/registry
  Component connection tracing
  Text logging
For very compact processors with no OS, developers can choose non-active components

## Slide 32: Status
Framework released as open source
Earlier JPL version flown on RapidScat, an ISS radar experiment
Has been ported to:
  Linux, MacOS, Windows (Cygwin), VxWorks, ARINC 653, RTEMS, Bare Metal (No OS)
  PPC, Leon3, x86, ARM (A15/A7), MSP430
Mature set of C&DH components
  Following flight processes such as code inspections, static analysis, and full-coverage unit testing
Version being developed as companion for JPL hardware project for Cubesat missions
  Will include platform driver components and other peripherals
Available on JPL GitHub:
  https://github.jpl.nasa.gov/FPRIME/fprime-sw.git
Hubs demonstrated on:
  Sockets
  ARINC 653 Channels
  High-speed hardware bus between nodes
  UARTs between nodes in an embedded system

## Slide 33: Advantages of the F´ Architecture
Autocoding:
  Component stubs and UTs
  Communication mechanics
Rapid Development:
  Rapidly swap components
  Multiple topologies and organizations
Standard Tooling:
  Application design tools
  System testing tools
Standard patterns and best practices at application level

## Slide 34: Open Source and F´
F´ Software Repository:
https://github.com/nasa/fprime
F´ Community Repositories:
https://github.com/fprime-community
F´ Internal Repository:
https://github.jpl.nasa.gov/FPRIME/fprime-sw
F´ Small Sat Introduction:
https://digitalcommons.usu.edu/smallsat/2018/all2018/328/
© 2009-2020 California Institute of Technology. Government sponsorship acknowledged.
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology,
under a contract with the National Aeronautics and Space Administration.
This software has been approved for open source release under NTR #49404.
Credit: NASA/KSC