## Slide 1: F`Software Framework A Small Scale Component Framework for Space
NASA Jet Propulsion Laboratory
5/29/2017
Copyright (C) 2009-2017 California Institute of Technology. ALL RIGHTS RESERVED.
Any commercial use must be negotiated with the Office of Technology Transfer at the California Institute of Technology.
The research was carried out at the Jet Propulsion Laboratory, California Institute of Technology,
under a contract with the National Aeronautics and Space Administration.
This software has been approved for open source release under NTR #49404.

## Slide 2: What is F`?
F` Flight Software Framework
  Targeted for instruments, CubeSats and other smaller platforms
  Currently baselined for Sphinx Leon3 Avionics SOC
A component-based architecture as well as a software framework to support it
  Software components
Designed from the ground up to be compact and reusable
Includes framework, code generators, build tools, Command/Telemetry GUI, and test environment
Designed to make it easier for developers to concentrate on mission-specific logic rather than common implementation patterns.

## Slide 3: Where is it being used?
Development
  Developed under JPL technology exploration task (2013)
  Matured under a number of JPL projects (2014-2017)
  Using established JPL flight processes/analysis tools
Flying on RapidScat (Launched 2014)
  Radar experiment on ISS
  No software bugs reported
Baselined for:
  Leonardo (Mars Helicopter Technology Development)
  Asteria (Cubesat)
  Lunar Flashlight (Cubesat)
  NEAScout (Cubesat)
Available on GitHub
  Reference example can be run on Linux, MacOS, Cygwin and most embedded ARM processors (e.g. Raspberry Pi)
  https://github.jpl.nasa.gov/FPRIME/fprime-sw.git

## Slide 4: F`: A Reusable Component Architecture
Consists of components (behaviors) and ports (interconnections for data)
Components are not dependent on other components, so can be reused.
Components to fulfill different requirements (simulation vs. actual) can be substituted, even at run time.
Components can have generic roles (commanding, telemetry, storage) which are not dependent on specific applications.
1
2
3
1
2
3
1
2
3

## Slide 5: F`: A Framework for quick development
F` provides a C++ framework and code generator that encapsulates:
  Thread management
  Inter-Process communication (IPC)
  Commanding
  Telemetry
  Parameters
Since these are common patterns, developer specifies in simple XML.
  Code generator generates boiler-plate code.
  Developer concentrates on domain-specific code.
  Framework invokes user code automatically
Component
1
2
3
Port 1
Port 2

## Slide 6: F`: A Framework for reuse
Over time, a library of reusable components are being built:
  For common facilities:
    Rate group management
    Command dispatching/sequencing
    Telemetry storage
    Ground interfaces
  For specific hardware platforms:
    Device drivers
    Radios
    GNC devices
    Operating system adaptations
A reusable ground system can be used
  Framework has uniform data representations
  Can be adapted to existing ground systems
    Runs on JPL multi-mission ground system
  Provided with Python-based lightweight ground system

## Slide 7: F`: A Portable Framework
Code base is in portable, embedded C++
Has abstraction layer for OS facilities such as:
  Threads
  Synchronization
  Files
  Time
Data products are stored and transmitted in a portable representation
  Allows interaction with ground system no matter the processor architecture
Has been run on the following processor architectures:
  X86, PPC, ARM, MSP430, Leon3
Has been run on the following OSes:
  VxWorks, RTEMS, Linux, MacOS, Cygwin, Raspberry Pi Raspbian
Very compact
  Framework classes ~1K compiled

## Slide 8: F`: A Framework for testing
F` components are decoupled from each other, so unit testing is easier
F` code generator generates counterpart test component that can be connected.
Test component “knows” the interfaces, commands, and telemetry
Tester can invoke generated C++ functions to exercise component interfaces, commands.
Telemetry automatically decoded and stored for checking in test component.
Component
1
2
3
Port 1
Port 2
Test Component

## Slide 9: F`: A Flight-ready Framework
For 2015-2016, C&DH components have been taken through flight software processes
  Design, coding and testing reviews with LARS tools and code coverage
    Design and code reviewed by peers
    Code scrubbed by static analyzers (e.g. Coverity)
    100% coverage except certain assertions (default switch, etc)
    Delivered with repeatable automated unit tests
  Includes:
    Rate Groups
    Command handling
    Command Sequencer
    Telemetry Processing
    Parameter storage
    Event handling
    File Uplink/Downlink
    Telemetry Database
    Health Monitor
    File Manager
    Socket “Ground” interface

## Slide 10: Both Ends of the Scale
TI MSP430
24K RAM
64K Flash
Rack Mount PC
Quad-core Xeon
8GB RAM
Hard disk